## Slide 1: High Speed Networks Introduction
Robert Iakobashvili,
Author: Akiva Sadovski from Broadcom
Spring 2022

## Slide 2: Introduction to Wide Area Networks
Agenda
  WAN?
  Why to focus on WAN?
  Evolution
  Benefits/business drivers
  Challenges and risks

## Slide 3: Wide Area Networks
LAN:
  Owned and managed by single organization
  Primary purpose: provide network access to hosts
WAN:
  Typically pay-for-service
  Provided and managed by regional telecommunications carriers
  Designed to interconnect networks

## Slide 4: Why to study WAN now?
Challenging
Next big thing
Happens right now

## Slide 5: Challenges
Complex topologies
Wild mix of technologies
Commodity

## Slide 6: Complex topologies
Telscom Consulting, Switzerland
Coax Cell
Optical
Access Network
CATV
Back Bone
WAN
Regional / Metro
(Data Back Bone)
Digital
&
Analog
HFC
Head-end
STM-4/16 speed level
CATV Cable Television
CGW Coax Gate Way
CM Cable Modem
CMT Cable Modem Termination
HFC Hybrid Fiber Coax
OADM Optical Add Drop Multiplexer
OANT Optical Access Network Termination
OXC Optical Cross Connect
SN Service Node
SOHO Small Offices, Home Offices
WAN Wide Area Network (all fiber)
STM-16/64 speed level
DWDM
Coax Cell
CGW
CM
Large
Enterprises
SN
SN
SN
Coax Cell
Digital
&
Analog
OANT
Digital
&
Analog
OANT
Digital
&
Analog
OANT
CGW
CGW
CGW
CGW
CGW
Coax
5 to 1000MHz
Downstream:
FDM (AM VSB, QAM)
Upstream:
FDMA/TDMA (QAM)
Service
Interfaces
House Wiring
LANs
Broadcast
Services
CGW
Residential
Medium Businesses
SOHO
Residential
Data Modems (CMTs) moving to the OANTs
Frequency Reuse in the Coax Distribution Cells
OXC
Router
OADM
Router
OADM
Router
OADM
Router

## Slide 8: Next big thing

## Slide 9: Happens right now
Significant transformation is taking place in data communications (MEF 2014):
  Deliver self-service, on-demand services over interconnected networks
  Enable the user to dynamically and on-demand, create, modify and delete services via customer web portals or software applications

## Slide 10: Life Cycle

## Slide 11: Hype

## Slide 12: Growth

## Slide 13: Evolution : ARPANET
1968: ARPANET was founded by the Advanced Research Projects Agency (ARPA) to serve as test bed for packet switching technology
197x:
  ARPANET evolved to consist of roughly 210 PSNs
  minicomputers interconnected point-to-point
1995 - NSF awarded MCI a contract to build a 155 Mb per second (Mbps) speed backbone

## Slide 14: Evolution : SONET/SDH
SONET=Synchronous optical network
SDH=Synchronous digital hierarchy
Standard for digital optical transmission
198x: Developed originally by Bellcore to allow mid-span meet between carriers: MCI and AT&T
You can lease a SDH connection from carriers

## Slide 15: SONET/SDH Highlights
Ideal for Voice: No queues. Guaranteed delay
Protection: Allows redundant Line or paths
Fast Restoration: 50ms using rings
Fixed Payload Rates: 51M, 155M, 622M, 2.4G, 9.5G
Rates do not match data rates of 10M, 100M, 1G, 10G
Static rates not suitable for bursty traffic
High Cost
Complex service set up

## Slide 16: Evolution: ATM
1980x: Research on Fast Packets
October 1991: ATM Forum founded

## Slide 17: ATM Highlights
Protocol layers
Connection identifiers
  Each cell contains a 24/28-bit connection identifier
  First 8/12 bits: Virtual Path, Last 16 bits: Virtual Channel
Connections via Channels
LAN Emulation
  Problem: need new networking SW for ATM
  Solution: let ATM network appear as LAN
  LAN emulation implemented below OS network layer

## Slide 18: ATM Challenge
High Cost
Complex service set up

## Slide 19: Ethernet: 10GbE
200x: main standardization effort
  Compatible with 802.3 frame format, services, management
  LAN and WAN distances
  Full-duplex only ⇒ No Shared Mode. Only switch based networks. No Hubs
  Same min and max frame size as 10/100/1000 Mbps

## Slide 20: Ethernet in WAN - Greenfield

## Slide 21: Ethernet in WAN - Legacy

## Slide 22: MPLS Timeline
Notes: IP addresses are allocated hierarchically: IP addresses that share the same prefix often share the same next hop. This reduces the routing table size and enhances scalability
When looking up a DIP in the routing table, several entries with different prefixes may match it.
The entry chosen is the one with the Longest Prefix Match (LPM)
HW LPM implementation was problematic in the 90-s
Therefore Cisco suggested to add a fixed length identifier to IP packets to speed up routing decisions

## Slide 23: Where it is used?
MPLS packets can run on Layer 2 technologies such as ATM, FR, PPP, PoS, Ethernet
Other Layer 2 technologies can be run over an MPLS network: Ethernet-over-MPLS, FrameRelay-over-MPLS etc
Currently, MPLS is a technology for delivery of IP Services:
  Virtual Circuit for IP: Unidirectional path (tunnel) through the network
  Traffic Engineering: Using paths other than the IGP shortest-path

## Slide 24: Label Switching Path
Notes: LER A:
Class Rule 1: PUSH 150
Class Rule 2: PUSH 100
LSR B:
ILM:
Ingress=eth1, InLabel=150, SWAP, OutLabel=250, Egress=eth2
Ingress=eth1, InLabel=100, SWAP, OutLabel=110, Egress=eth2
LSR C:
ILM:
Ingress=eth1, InLabel=250, SWAP, OutLabel=350, Egress=eth2
Ingress=eth1, InLabel=110, SWAP, OutLabel=120, Egress=eth3
LER D
ILM:
Ingress=eth1, InLabel=350, POP, OutLabel=N/A, Egress=eth2
LER D
ILM:
Ingress=eth1, InLabel=120, POP, OutLabel=N/A, Egress=eth2

## Slide 25: Next Step
2004 - Software Defined Networks
201x – Network Functions Virtualization
201x –SD-WAN

## Slide 26: SDN in a nutshell
Source: Nick McKeown Stanford University

## Slide 27: Vision for NFV
Source: ETSI

## Slide 28: Bringing SDN to WAN

## Slide 29: Business drivers
On-demand Services
  activation times which can no longer take days or weeks
Expectation for Quality
  users expect the performance of their apps in the remote cloud to behave as they do when running locally on their LAN
Value Perception
  network becomes practically invisible until it negatively impacts the application experience
Network Abstraction Reduces Headaches
  applications running on the standard hardware

## Slide 30: Risks and challenges
Managing the WAN
Security policies
Performance

## Slide 31: Network Node – Packet Classification
  Exact Match
  Prefix Matching
  Content Addressable Memory
  Multi Field Prefix Matching

## Slide 32: Network Node – Queue Management
  Tail Drop
  Random Early Discard (RED)
  Fair Random RED
  QCN – Quantized Congestion Notification
  CHOKE algorithm

## Slide 33: Network Node – Packet Scheduling
  FIFO queueing
  Strict priority
  Round Robin
  Deficient Round Robin
  Generalized Processor Sharing (GPS) and Weighted Fair Queue
  Hierarchical scheduling

## Slide 34: Traffic Metering and Marking
Single Rate Three Color Marker
Two Rate Three Color Marker
Etc

## Slide 35: Network Node – Switch Fabric
General Switch Architecture; Blocking
Switching Fabric
  Time division switching
  Space division switching
  Virtual Output Queuing
  Take a Ticket
  Parallel Iterative Matching
  iSLIP

## Slide 36: Network Node – Multistage Switch Fabric
Clos Network
Clos Network Heuristics: Concurrent Round-Robin-Dispatching (CRRD)
Banyan Network
Congestion in Delta Networks
Benes Network

## Slide 37: Real World Examples from Linux Kernel
5332883.html

## Slide 38: Quality of Service
Integrated Services
  Reservation Protocol (RSVP)
Differentiated Services (DiffServ)
  Per Hop Behavior (PHB)
  Expedited Forwarding
  Assured Forwarding

## Slide 39: MPLS
Intro to Multi Protocol Label Switching
Label Switching Path (LSP)
MPLS Label and Label Stacking
Inside MPLS Router
LSP Tunnels
MPLS Data Plane and Control Plane
Label Distribution Protocol

## Slide 40: Advanced MPLS and MPLS applications
Introduction to Traffic Engineering (TE)
MPLS Fast Re-Route (FRR)
Pseudowire (PW)
Virtual Private Networks
MPLS Transport Profile (MPLS-TP)

## Slide 41: Virtual Private Networks
Pseudowires and pseudowire encapsulations over MPLS
L2 Virtual Private Networks
  Virtual Private Wire Service
  Virtual Private LAN Service
MPLS L3 VPN

## Slide 42: Software Defined Networks (SDN)
Rationale behind SDN
Software-Defined Networking Architecture
Data Plane – Control Plane separation
OpenFlow

## Slide 43: Final Assessment
50% - Final coursework
50% - Exam

## Slide 44: Homework 1
Simulator
  Mininet: http://mininet.org/ written in Python, extendable by writing add-ons in Python
Build simple topology:
Experiment with it

## Slide 45: Homework 2
Mininet
Real world Network Simulation
Throughput and packet delay measurements

## Slide 46: Materials to be submitted
Model-related software. Generally it will be a single Python script implementing the Mininet model; provide any other SW if required
One page report with short description and results

## Slide 47: Coursework
?

## Slide 48
Network taxonomy

## Slide 49: Multiple Access Links and Protocols
Three types of “links”:
point-to-point (single wire, e.g. PPP, SLIP)
broadcast (shared wire or medium; e.g Ethernet)
switched (e.g., switched Ethernet, ATM etc)

## Slide 50: Nodes
Nodes may connect:
  To other nodes only, or
  To stations and other nodes
Network is usually partially connected
  Some redundant connections are desirable for reliability
Two different switching technologies
  Circuit switching
  Packet switching

## Slide 51: Switching Networks
Long distance transmission is typically done over a network of switched nodes
Nodes not concerned with content of data
End devices are stations
  Computer, terminal, phone, etc
  A collection of nodes and connections is a communications network
Data is routed by being switched from node to node

## Slide 52: Information
The world doesn't run on bits, bytes, circuits, or even packets
Source http://itsallaboutembedded.blogspot.co.il/

## Slide 53: Circuit switching - 1
Circuit switching was the first switching technique used in communication networks because it is simple enough to carry analog signals
Circuit switching was designed in 1878 in order to send telephone calls down a dedicated channel
In circuit switching, the transmission medium is typically divided into channels using Frequency Division Multiplexing (FDM), Time Division Multiplexing (TDM) or Code Division Multiplexing (CDM)
This channel remains open and in use throughout the whole call and cannot be used by any other data or phone calls

## Slide 54: Circuit Switching - 2
Dedicated communication path between two stations
Three phases:
  Establish
  Transfer
  Disconnect
Must have switching capacity and channel capacity to establish connection
Must have intelligence to work out routing
Once connected, transfer is transparent

## Slide 55: Circuit switching – circuit establishment
To establish the circuits, a signaling mechanism is used
Signaling is the process of exchanging messages within the control plane to
  set up
  maintain
  modify
  terminate
  data paths in the data plane
It is the most complex part in circuit switching

## Slide 56: Circuit switching – bandwidth reservation
In circuit switching the channel bandwidth is reserved for an information flow
To ensure timely delivery of the data, the capacity of the circuit has to be at least equal to the peak transmission rate of the flow

## Slide 57: Circuit switching – call blocking
If there are not enough channels for the request, the call establishment may be :
  delayed
  blocked
  dropped
In contrast, once the call is accepted, resources are not shared with other flows, eliminating any uncertainty

## Slide 58: Circuit switching drawbacks
Circuit switching designed for voice
  Resources dedicated to a particular call
  Much of the time a data connection is idle
  Data rate is fixed
Both ends must operate at the same rate

## Slide 59: Packet Switching: Basic Operation
Data transmitted in small packets
  Typically 1000 octets
  Longer messages split into series of packets
  Each packet contains a portion of user data plus some control info
Control info
  Routing (addressing) info
Packets are received, stored briefly (buffered) and past on to the next node
  Store and forward

## Slide 60: Packets
Packet networking is the translocation of data between distributed computational processes
The packets are arbitrary divisions of data flows, and should not be treated like physical objects
The packets are repeatedly duplicated and erased

## Slide 61: Packets, frames, etc
Packet – small portion of data and corresponding headers, usually L3 and higher
Frame – L1 and L2
Buffer – area in the node’s memory allocated for a frame or a packet storage

## Slide 62: Use of Packets

## Slide 63: Packets Switching Advantages
Line efficiency
  Single node to node link can be shared by many packets over time
Packets queued and transmitted as fast as possible
Data rate conversion
  Each station connects to the local node at its own speed
  Nodes buffer data if required to equalize rates
Packets are accepted even when network is busy
  Delivery may slow down
Priorities can be used

## Slide 64: Packet Switching Techniques
Station breaks long message into packets
Packets sent one at a time to the network
Packets handled in two ways
  Datagram
  Virtual Circuit (VC)

## Slide 65: Datagram
Each packet treated independently
Packets can take any practical route
Packets may arrive out of order
Packets may go missing
Up to receiver to re-order packets and recover from missing packets

## Slide 66: Virtual Circuit
Preplanned route established before any packets sent
Call request and call accept packets establish connection (handshake)
Each packet contains a virtual circuit identifier instead of destination address
No routing decisions required for each packet
Clear request to drop circuit
Not a dedicated path

## Slide 67: Bringing it all together

## Slide 68: Synchronous and Asynchronous Transmission - Hierarchy
Hierarchy of synchronization tasks:
  Bit level: recognizing the start and end of each bit
  Byte (character) level
  Block or message level: recognize the start and end of each unit of data (in networks this is a frame)
A fundamental requirement of digital data communications is that the receiver knows the starting time and the duration of each bit

## Slide 69: Asynchronous Transmission
  each character (or byte) is treated independently for clock (bit) and character (byte) synchronization purposes
  the receiver resynchronizes at the start of each character received.

## Slide 70: Synchronous Transmission
  A continuous stream of data signals is accompanied by timing signals (generated by an electronic clock)
  Ensures that the transmitter and the receiver are in step (synchronized) with one another
  The data is sent in blocks (called frames or packets) spaced by fixed time intervals

## Slide 71: Multiplexing
Several link connections of client layer networks supported by one server layer trail at the same time
Source: ITU-T Recommendation G.805

## Slide 72: Inverse multiplexing
Client layer link connection is supported by several server layer trails in parallel
Source: ITU-T Recommendation G.805

## Slide 73: Monitoring techniques
Connection may be indirectly monitored by using the data inherently available from the server layer
Non-intrusive monitoring
Intrusive monitoring
Sublayer monitoring: some portion of the original capacity is overwritten by the test signal

## Slide 74: Partitioning and layering
A transport network can be decomposed into a number of independent transport layer networks with a client/server association between adjacent layer networks
Each layer network can be separately partitioned in a way which reflects the internal structure of that layer network or the way that it will be managed
Source: ITU-T Recommendation G.805

## Slide 75: Layering
When standard networks were first proposed it was realized that the subject was so complex that it had to be broken down into more readily digestible parts
Layering is employed despite the fact that it significantly reduces the efficiency of communications networks
For example, in a VoIP application one may go to great lengths to compress 10 milliseconds of telephony quality speech from 80 Bytes down to 10 Bytes, but to that payload:
  one then adds an RTP header of at least 12 bytes
  a UDP header of 8 bytes
  an IPv4 header of 20 bytes
  an Ethernet header and trailer of at least 18 bytes
for a grand total of at least 48 bytes of overhead

## Slide 76: Layer network interworking
The objective of layer network interworking is to provide an end-to-end trail between different types of layer networks
The interworking link connection is special in the sense that it is asymmetric, delimited by different types of ports
Source: ITU-T Recommendation G.805

## Slide 77: Partitioning
The partitioning defines:
administrative boundaries between network operators jointly providing connections within a single layer network
domain boundaries within a layer network of a single operator to allow the apportioning of performance objectives to the architectural components

## Slide 78: Subnetworks
A subnetwork is defined as an arbitrary collection of (usually connected) nodes or subnetworks
The most basic subnetwork consists of a single node
Subnetworks can be nested
Source: GMPLS: Architecture and Applications by Adrian Farrel and Igor Bryskin

## Slide 79: Questions?