## Slide 1: High Speed Networks Switches and Switching Algorithms
Robert Iakobashvili,
Author: Akiva Sadovski from Broadcom
Spring 2022

## Slide 2: Ethernet Switch/Router architecture overview
Source: Cisco Nexus 5548P Switch Architecture © 2010 Cisco

## Slide 3: Requirements
Capacity of switch is the maximum rate at which it can move information, assuming all data paths are simultaneously active
Primary goal: maximize capacity – work at wire speed at all ports
  subject to cost and reliability constraints
Circuit switch must reject call if can’t find a path for samples from input to output
  goal: minimize call blocking
Packet switch must reject a packet if it can’t find a buffer to store it awaiting access to output trunk
  goal: minimize packet loss
Subgoal: Don’t reorder packets

## Slide 4: Basic concepts
Accessibility
Blocking
Complexity
Scalability
Reliability
Throughput

## Slide 5: Accessibility
A network has full accessibility (=connectivity) when each ingress can be connected to each egress
A network has a limited accessibility when the above property does not exist
Interconnection networks applied in today’s switch fabrics usually have full accessibility

## Slide 6: Blocking: definition and types
Blocking means that it is possible that no connection can be set between the idle input/output pair
Class | Type | Switch state
Non-blocking | Strict sense non blocking | Without blocking states
 | Wide sense non blocking | With blocking states
 | Rearrangeably non blocking | 
Blocking | Others | 

## Slide 7: Definition of blocking types
Strict-sense non-blocking - a path can always be set up between any idle ingress and any idle egress without disturbing paths already set up
Wide-sense non-blocking - a path can be set up between any idle ingress and any idle egress without disturbing existing connections, provided that certain rules are followed. These rules prevent network from entering a state for which new connections cannot be made
Rearrangeably non-blocking - when establishing a path between an idle ingress and an idle egress, paths of existing connections may have to be changed (rearranged) to set up that connection

## Slide 8: Complexity
Complexity of an interconnection network is expressed by cost index
Traditional definition of cost index gives the number of cross-points in a network
  used to be a reasonable measure of space division switching systems
Nowadays cost index alone does not characterize cost of an interconnection network for broadband applications
  VLSIs and their integration degree has changed the way how cost of a switch fabric is formed (number of ICs, power consumption)
  management and control of a switching system has a significant contribution to cost

## Slide 9: Scalability
Due to constant increase of transport links and data rates on links, scalability of a switching system has become a key parameter in choosing a switch fabric architecture
Scalability describes ability of a system to evolve with increasing requirements

## Slide 10: Reliability, Availability, Fault Tolerance
Reliability defines probability that a system does not fail within a given time interval provided that it functions correctly at the start of the interval.
Availability defines probability that a system will function at a given time instant
Fault tolerance is the capability of a system to continue its intended function in spite of having a fault(s)
Reliability measures:
  MTTF (Mean Time To Failure)
  MTTR (Mean Time To Repair)
  MTBF (Mean Time Between Failures)
Reliability and fault tolerance are system measures that have an impact on all functions of a switching system
Notes: אמינות, זמינות ועמידות לתקלות

## Slide 11: Throughput and speedup
The throughput of the switch fabric is defined as the ratio of the:
  Average aggregate output rate to
  Average aggregate input rate
A speedup of k means that the internal forwarding rate of the switch fabric is k times the input line rate
Notes: האצה
תפוקה

## Slide 12: Blocking in packet switch
Can have both internal and output blocking
Internal
  no path to output
  Example: head of line blocking
Output
  output link busy
Output blocking is also called the output contention

## Slide 13: Dealing with the blocking
Overprovisioning
  internal links much faster than inputs
Buffers: if packet is blocked, the switch must either buffer or drop it
  at input, switch fabric itself or at the output
Backpressure
  if switch fabric doesn’t have buffers, prevent packet from entering until path is available
Parallel switch fabrics
  increases effective switching capacity

## Slide 14: Dealing with the scalability
A large scale switch is built with multiple switch modules interconnected in different structures
They are partitioned into:
  Single stage
  Multistage

## Slide 15: First generation switch
Most Ethernet switches and cheap packet routers
Bottleneck can be CPU, host-adaptor or I/O bus
computer
queues in memory
CPU
linecard
linecard
linecard

## Slide 16: Second generation switch
Port mapping intelligence in line cards
Bottleneck is the bus (or ring)
bus
computer
front end processors
or line cards

## Slide 17: Third generation switches
Third generation switch provides parallel paths (fabric)
NxN
packet
switch
fabric
OLC
OLC
OLC
IN
ILC
ILC
ILC
OUT
control

## Slide 18: Third generation switches: the features
  self-routing fabric
  output buffer is a point of contention
    unless we arbitrate access to fabric
  potential for unlimited scaling
    as long as we can resolve contention for output buffer

## Slide 19: Store-and-forward and cut-through Layer 2 switches
Both base their forwarding decisions on the destination MAC address of data packets;
Store-and-forward
  makes a forwarding decision on a data packet after it has received the whole frame and checked its integrity
  Ingress buffering: flexibility to support any mix of Ethernet speeds, starting with 10 Mbps
  Access Control Lists
Cut-through
  a cut-through switch can make a forwarding decision as soon as it has looked up the DMAC address of the data packet
  A cut-through switch may parse an incoming packet until it has collected enough information from the frame content to make more sophisticated forwarding decision
Notes: a cut-through switch can quickly decide whether it needs to examine a larger portion of the packet
headers. It can parse past the first 14 bytes (the SMAC, DMAC, and EtherType) and handle, for
example, 40 additional bytes in order to perform more sophisticated functions relative to IPv4
Layer 3 and 4 headers. At 10 Gbps, it may take approximately an additional 100 nanoseconds to
receive the 40 bytes of the IPv4 and transport headers.

## Slide 20: Switching Fabric

## Slide 21: The Place of Switching Fabric

## Slide 22: Space Switching: an abstract model

## Slide 23: Multiplexors and demultiplexors - 1
Multiplexor: aggregates sessions
  N input lines
  Output runs N times as fast as input
Demultiplexor: distributes sessions
  one input line and N outputs that run N times slower

## Slide 24: Multiplexors and demultiplexors - 2

## Slide 25: Multiplexors and demultiplexors - 3

## Slide 26: Time division switching
Key idea: when demultiplexing, position in frame determines an output link
Time division switching interchanges sample position within a frame

## Slide 27: Time Slot Interchange

## Slide 29: Time Division Switching Pros and Cons
Pros
  Simple to build.
  Multicast: easy (why?)
Cons
  Limit is the time taken to read and write to memory
  For 120,000 telephone circuits
    Each circuit reads and writes memory once every 125 ms
    Number of operations per second : 120,000 x 8000 x2
    each operation takes around 0.5 ns => impossible with current technology

## Slide 30: Space division switching
Each sample takes a different path through the switch, depending on its destination
Crossbar: Simplest possible space-division switch
Crosspoints can be turned on or off
1
2
3
4
1
2
3
4
sessions: (1,2) (2,4) (3,1) (4,3)
inputs
output

## Slide 31: Time-Space: Example
2 1
4 3
TSI
2 1
3 4
3
1
2
4
Internal speed = double link speed
time 2
TSI
time 1

## Slide 32: Buffering strategy in Switching Fabrics
Buffers are required to temporary store packets or cells to lose the congestion
Buffering strategies:
  Shared Memory Queuing
  Output Queuing (OQ)
  Input Queuing
  Virtual Output Queuing (VOQ)
  Combined Input and Output Queuing (CIOQ)
  Crosspoint Queuing

## Slide 33: Shared-Memory Queuing
The memory unit is used to store cells for all output ports
The memory contains N output queues, one per output port
Each queue stores the cells destined for the corresponding output

## Slide 34: Output Queuing
Cells are immediately forwarded to the destined output ports once they arrive at the inputs
Buffers are needed at the output ports
Benefit: better QoS
Drawbacks:
  Memory speed constrains
  Switch side limitations

## Slide 35: Input Queuing
One FIFO per input port
Only one cell heading to an output port can be forwarded per time slot
Head of Line (HoL) blocking

## Slide 36: Virtual Output Queuing
Cells are buffered at input ports
The input buffer is divided into N logical queues (VOQs) storing the cells destined to the associated output port
Eliminates HoL blocking

## Slide 37: Combined Input and Output Queuing
Switch fabric operates faster than the line rate
Each output can receive more than one cell in each timeslot
Notes: It is proved that with the speedup of four, the CIOQ switch can achieve the 99% throughput

## Slide 38: Crosspoint Queuing
A buffer can be placed at each crossbar
Pros: no HoL blocking
Cons: no buffers sharing, N2 discrete buffers
Source: INFOCOM 2009, IEEE
Kanizo, Y. ; Dept. of Comput. Sci., Technion - Israel Inst. of Technol., Haifa

## Slide 39: Take a Ticket - definition
Each output line card S maintains a distributed queue for all input line cards R waiting to send to S
The queue for S is actually stored at the input line card itself (instead of being at S) using a simple ticket number mechanism

## Slide 40: Take a Ticket – operation guidelines
Line card R wants to send a packet to line card S:
  makes a request over a separate control bus to S
  S provides a queue number back to R over the control bus
  The queue number is the number of R’s position in the output queue for S
  R then monitors the control bus; whenever S finishes accepting a new packet, S sends the current queue number it is serving on the control bus
  R notices that its number is being “served,” – R places its packet on the input data bus for R. At the same time, S ensures that the R–S crosspoint is turned on

## Slide 41: Take a Ticket – operation example

## Slide 42: Take a Ticket – pros and cons
Pros
  Scales well in control state, requiring only two (log2N)-bit counters at each output port to store the current ticket number being served and the highest ticket number dispensed
  Able to handle variable-size packets directly
Cons
  Head Of Line blocking
  Cannot handle multicast

## Slide 43: Take a Ticket – Hunt Group
Any set of line cards (not just physically contiguous line cards) can be aggregated to form an effectively higher-bandwidth link called a hunt group
The next packet destined to the group is served by the first free output port in the hunt group
Notes: While basic hunt groups can cause reordering of packets
sent to different links, a small modification allows packets from one input to be sent to only
one output port in a hunt group via a simple deterministic hash. This modification avoids
reordering, at the cost of reduced parallelism

## Slide 44: Head of Line blocking avoidance
Allowing an input port to schedule not just the head of its input queue, but also other cells, which can make progress when the head is blocked
Do not schedule any cells other than the first cell sent to every distinct output port
Provide a separate input queue per output at each input port - virtual output queue(VOQ)

## Slide 45: Communicating the scheduling needs
Communicating the scheduling needs of any input port takes a bitmap of only N bits, where N is the size of the switch
A 1 in position i implies that there is at least one cell destined to output port i
The scheduler needs to process only N2 bits

## Slide 46: Parallel Iterative Matching operation example
Notes: Resolving output-port contention is insufficient because there is also input port contention.
Two output ports can randomly grant to the same input port, which must
choose exactly one to send a cell to.

## Slide 47: PIM Input Utilization
Probability that an input port receives at least one grant is equal to one (1) minus the probability that all outputs grant one of the remaining inputs:

## Slide 48: Iterative Matching
If ports 1, 2, and 3 all choose A, the match size will only be of size 2
The algorithm shall mask out all matched inputs and outputs and iterate more times (for the same forthcoming time slot)
If the match on the current iteration is not maximal, a further iteration will improve the size of the match by at least 1

## Slide 49: Avoiding randomization with iSlip
PIM “derandomization”
iSLIP provides fairness by choosing the next winner among multiple contenders in round-robin fashion using a rotating pointer
Each output maintains a pointer g initially set to the first input port
The output chooses the lowest input number that is equal to or greater than g
Each input port maintains a pointer a initially set to the first output port
When an input port has to choose between multiple output-port grants, it chooses the lowest output port number that is equal to or greater than a

## Slide 50: iSLIP operation example - 1
Source: Network Algorithmics by George Varghese
Notes: The second iteration starts with only inputs unmatched on
previous iterations (i.e, B) requesting and only to hitherto unmatched outputs. Thus B requests
to 2 and 3 (and not to 1, though B has a cell destined for 1 as well). Both 2 and 3 grant B, and
B chooses 2 (the lowest one that is greater than or equal to its accept pointer of 1). One might
think that B should increment its accept pointer to 3 (1 plus the last accepted, which was 2).
However, to avoid starvation iSLIP does not increment pointers on iterations other than the
first, for reasons that will be explained.
Thus even after B is connected to 2 2’s grant pointer remains at A and 2’s accept pointer
remains at 1. Since this is the final iteration, all matched pairs, including pairs, such as A,1,
matched in prior iterations, are all connected and data transfer (solid lines) occurs.

## Slide 51: iSLIP operation example - 2
Source: Network Algorithmics by George Varghese

## Slide 52: Extending iSLIP to handle priorities
Each output port keeps a separate grant pointer gk for priority level k, and each input port keeps a separate accept pointer ak for each priority level k.
The iSLIP algorithm is performed with each entity (input port, output port) performing the iSLIP algorithm on the highest-priority level among inputs it sees

## Slide 53: Extending iSLIP to handle multicast
Multicast uses only one queue and, as such, is subject to some HOL blocking because a multicast packet cannot begin to be processed unless the multicast packets ahead of it are sent
ESLIP maintains only a shared multicast grant pointer and no multicast accept pointer at all
Notes: However, unlike unicast scheduling, the grant pointer for multicast is not incremented to
1 past I until I completes its fanout.
How should an output port balance between multicast and unicast packets? ESLIP does so by giving multicast
and unicast traffic higher priority in alternate cell slots.

## Slide 54: Two Stage Network
Only one cell can be transmitted between any pair of modules (only one path between them)
Very high blocking probability

## Slide 55: Fat Network example - Clos Network
Multistage circuit switching network, first formalized by Charles Clos in 1953
Clos networks have three stages:
  ingress stage (A)
  middle stage(B)
  egress stage (C )
The routing problem: how to direct the input packets/cells to the respective outputs without conflicts
Notes: Each ingress stage crossbar switch has m outlets, and there are m middle stage crossbar switches. There is exactly one connection between each ingress stage switch and each middle stage switch. There are r egress stage switches, each with m inputs and n outputs. Each middle stage switch is connected exactly once to each egress stage switch. Thus, the ingress stage has r switches, each of which has n inputs and m outputs. The middle stage has m switches, each of which has r inputs and r outputs. The egress stage has r switches, each of which has m inputs and n outputs.

## Slide 56: Routing in Clos Network
The routing problem in Clos network interpreted as three equivalent questions:
  How to assign central routes in a Clos network with m central modules to accommodate a set of connection requests?
  How to edge color a given bipartite graph with maximum degree m?
  How to decompose a matrix with row/column sum ≤ m into m matrices with row/column sum ≤ 1?

## Slide 57: Clos Network: edge coloring in bipartite graph
Matching algorithms has a linear complexity O(N)

## Slide 58: Clos Network: matrix decomposition
Each of sub-matrices must have the following property:
and
Source: High Performance Switches and Routers H. Jonathan Chao, Bin Liu May 2007, Wiley-IEEE Press

## Slide 59: Clos Network Heuristics: Concurrent Round-Robin-Dispatching (CRRD)
IM - Input module at the first stage.
CM - Central module at the second stage.
OM - Output module at the third stage.
n - Number of input/output ports (IPs)/OPs in each IM/OM, respectively.
k - Number of IMs/OMs.
m - Number of CMs.
Source: High Performance Switches and Routers H. Jonathan Chao, Bin Liu May 2007, Wiley-IEEE Press

## Slide 60: Clos Network CRRD phase 1
Matching within IM:
  Step 1: At each time slot, each nonempty VOQ sends a request to every output-link arbiter.
  Step 2: Each output-link arbiter chooses one nonempty VOQ request in a round-robin fashion
  Step 3: The VOQ arbiter sends the accept to the granting output-link arbiter among all those received in a round-robin fashion
Source: High Performance Switches and Routers H. Jonathan Chao, Bin Liu May 2007, Wiley-IEEE Press

## Slide 61: Clos Network CRRD phase 2
Matching between IM and CM
Step 1: A request that is associated with LI(i,r) is sent out to the corresponding CM(r). A CM(r) has output links , each of which corresponds to an OM(r). An arbiter that is associated with LC(r,j) selects one request among k requests.
Step 2: If a VOQ at the IM receives the grant from the CM, it sends the corresponding cell at next time slot.
Source: High Performance Switches and Routers H. Jonathan Chao, Bin Liu May 2007, Wiley-IEEE Press
Notes: LI(i,r) – r-th outgoing link of IM(i)
LC(r,j) – j-th outgoing link of CM(r)

## Slide 62: Clos Network CRRD arbitration

## Slide 63: Difference between CRRD and iSLIP
in CRRD: a VOQ sends a request to every output-link arbiter
in iSLIP: a VOQ sends a request to only the destined output-link arbiter

## Slide 64: Clos Network - strict sense non-blocking
Holds for m  2n-1
Proof:
  Consider an idle input and output
  Input box connected to at most n-1 middle layer switches
  output box connected to at most n-1 middle layer switches
  There exists an ”unused" middle switch good for both.
n x m
m x n
n-1
n-1

## Slide 65: Clos Network - re-arrangeable
If m ≥ n, the Clos network is re-arrangeably non-blocking, meaning that an unused input on an ingress switch can always be connected to an unused output on an egress switch, but for this to take place, existing calls may have to be rearranged by assigning them to different center stage switches in the Clos network
Proof:
  Consider the routing graph.
  find a perfect matching.
  route the perfect matching through a single middle switch!
  remaining network is Clos(m-1,n-1,r-1)

## Slide 66: Banyan Network
It is named for its resemblance to the roots of the banyan tree which cross over in complex patterns
In Hinduism, the leaf of the Banyan tree is said to be the resting place for the god Krishna
In Buddhism's Pali canon, the banyan (Pali: nigrodha) is referenced numerous times

## Slide 67: Banyan (Delta) Network
Recursively constructed of:
  Two smaller (N/2)-size Delta networks
  a first stage of 2-by-2 switches
If the output is in the upper half (MSB of output is 0), then the input is routed to the upper N/2 Delta Network
If the output is in the lower half (i.e., MSB=1), the input is routed to the lower N/2 Delta network

## Slide 68: Banyan Network: unwinding the recursion

## Slide 69: Banyan (Delta) Networks properties
Self-routing
  the unique path from a given input to a given output o=o1,o2,...,os expressed in binary can be found by following the link corresponding to the value of oi in stage I
Reversible
  It is possible to trace a path from an output to an input by following bits of the input in the same way

## Slide 70: Congestion in Delta Networks
There is a unique path from each input to each output
If each successive pair of inputs wishes to send a cell to the same output half, only half of the cells can proceed to second stage

## Slide 71: Conditions for non-blocking operation of Banyan network
No idle input between any two active inputs
Output addresses of the cells are in either an ascending or descending order

## Slide 72: Sort Banyan Network

## Slide 73: Batcher Sorting Network
A sorting network is formed by a series of merge networks

## Slide 74: Broadcast Banyan Network
A broadcast Banyan Network is a Banyan Network with switches capable of replicating cells

## Slide 75: Benes Network
Third stage of 2-by-2 switches
These third stages to the two (N/2)-sized networks in the middle in the same way as the first-stage switches are connected to the two middle (N/2)-sized networks

## Slide 76: Benes Network
The left half is a standard Delta Network
The right half is a mirror reversed Delta Network
Source: Network Algorithmics by George Varghese

## Slide 77: Resources
Network Algorithmics: An Interdisciplinary Approach to Designing Fast Networked Devices by George Varghese (The Morgan Kaufmann Series in Networking) ISBN-13: 978-0120884773 December 29, 2004
High Performance Switches and Routers by H. Jonathan Chao and Bin Liu ISBN: 978-0-470-05367-6 May 2007, Wiley-IEEE Press
Concurrent Round-Robin-Based Dispatching Schemes for Clos-Network Switches, by Eiji Oki, Member, IEEE, Zhigang Jing, Member, IEEE, Roberto Rojas-Cessa, Member, IEEE, and H. Jonathan Chao, Fellow, IEEE http://eeweb.poly.edu/labs/hsnetworking/docs/public/concurrent.pdf
Parallel Routing Algorithms in Benes-Clos Networks, by Tony T. Lee and Soung-Yne Liew http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=497904&url=http%3A%2F%2Fieeexplore.ieee.org%2Fiel2%2F3539%2F10628%2F00497904.pdf%3Farnumber%3D497904

## Slide 78: Questions?