## Slide 1: Traffic Engineering and BGP
Subtitle

## Slide 2: Traffic Engineering
RFC 2702,Requirements for Traffic Engineering Over MPLS:
    traffic engineering is a technology that is concerned with performance optimization of operational networks

## Slide 3: ISP Relationships
customer-provider
peer-peer
backup

## Slide 4: BGP Decision Process
Consists of an ordered list of attributes across which routes are compared
The ordering of attributes allows the operator to influence various stages of the decision process
Attribute can be set
  Locally
  Neighbor
  Neither
3 steps a router use to process advertisements:
  Import policy
  Decision process
  Export policy

## Slide 5: Configuring Local Policies
Preference - Changing preference is done by adding/deleting/modifying route attributes in BGP advertisements
Filtering
Tagging - The key mechanism is the community attribute, a variable-length string used to tag routes
ISP implements its policies by applying configuration commands at routers
Configurations typically consist of a set of lists of preference, filtering, and tagging rules, one list for each session the router has with a neighboring BGP-speaking router

## Slide 6: Route Map
A language construct
Route Map – key primitive
  Consists of two parts:
    a set of conditions indicating when the map is to be invoked
      the prefix is a specified value, or
      the AS path matches a specified regular expression
    the action to be taken if the advertisement matches the conditions

## Slide 7: Traffic Engineering Goals
early exit routing - ISP forwards traffic to its closest possible exit point to reduce the number of links packets traverse
load balancing traffic over several links when possible
Inbound Traffic Control – how much traffic ISP receives from each of its peering links
  can be done by modifying the MED attribute

## Slide 8: Traffic Engineering Techniques
Assigning nonoverlapping range of LocalPref values to each type of peering relationship
  90–99 might be used for customers
  80–89 for peers
  70–79 for providers
  60–69 for backup links
Controlling Route Export
  configures an import policy that appends the community attribute Xpeer- - to indicate that the route was received from a peer
Remote Control
by configuring routers to map certain community attributes to certain LocalPref values